## Slide 1
FUN SPHERE
Kids Interactive Gaming System
Mostafa Ahmed Abd El Monem | 23P0423
Ahmed Elbaramawy | 24P0203
Omar Khaled Aly Ibrahim Gaballa | 22P0238
Ahmed Khaled Ahmed | 24P0133
Supervisor: Dr. Shady Ahmed Maged Ahmed Mohamed
Dept. of Mechatronics Engineering — Ain Shams University

## Slide 2
ABSTRACT
10
Total Balls
(5 white + 5 black)
2–10
Target Age
Range (years)
3D
Printed Parts
(PLA filament)
This project presents a fully functioning electromechanical toy for children aged 2–10. Players control adjustable cannons to shoot coloured balls into a basket. An Archimedes screw lifts balls, infrared sensors detect colour, and a servo motor sorts them. Scores update in real-time on an LCD screen and a mobile application. Parts are designed in Autodesk Inventor 2024 and manufactured via 3D printing and laser cutting.

## Slide 3
INTRODUCTION
🎯 Cannon System
Adjustable cannons allow players to aim and shoot balls towards a target basket, enhancing hand-eye coordination.
⬆️ Ball Lifting Mechanism
Missed and scored balls are collected and lifted back using an Archimedes screw mechanism for continuous play.
🔴 Sorting Mechanism
Infrared sensors detect ball colour; a servo motor classifies and routes them to the correct team lane.
📊 Scoreboard & Interface
Scores are updated in real-time on an LCD screen and a companion mobile application.

## Slide 4
SYSTEM ARCHITECTURE
Lifting
Archimedes screw
mechanism lifts balls
back for replay
Shooting
Adjustable cannon
aims & launches
balls at the basket
Sorting
IR sensor + servo
motor classifies
balls by colour
Mobile
App
Real-time score
updates via
Bluetooth/WiFi
PCB
Design
Custom PCB with
two Arduino MCUs
and LCD display

## Slide 5
WHOLE SYSTEM FLOWCHART
START / Power ON
Load balls into cannons
Player aims & shoots cannon
Ball enters
basket?
YES
NO
Missed shot →
collected in lane
IR sensor 1 detects ball colour
MCU 1
Announce score
MCU 2
Update LCD
Archimedes screw lifts ball
IR sensor 2 identifies colour
Servo motor sorts ball to
correct team lane
Game
over?
YES
NO
END / Display Final Score

## Slide 6
PROJECT PLAN & TOOLS
📋 Project Deliverables
WBS (Work Breakdown Structure)
Gantt Chart
PDS – Product Design Specifications
Whole System Flowchart
Whole System Block Diagram
Wiring Diagrams (per subsystem)
PCB Design Schematic
🛠 Tools & Software
Autodesk Inventor 2024 (3D CAD)
Fritzing (PCB design)
Arduino IDE (firmware)
ClickUp (project management)
Tinkercad (circuit simulation)
3D Printer & Laser Cutter

## Slide 7
CONCLUSION
Merges entertainment with education for children aged 2–10
Hand-eye coordination & problem-solving through interactive gameplay
Four cohesive subsystems: shooting, lifting, sorting & scoring
Adheres to ergonomic and child safety standards
Eco-friendly PLA materials — aligns with sustainability goals
Modular design enables easy maintenance and mass production
Dept. of Mechatronics Engineering — Ain Shams University